## Slide 1
Deviations from literature
Low T density check
Update of Latest Data
Error Propagation
Manuscript draft process
Summary

## Slide 2
Some data differences from Giauque and others
Deviations from TRF

## Slide 3
Seem to suggest a gradient offset
Next steps? Modify TRF equation?
Deviations from TRF

## Slide 4
Lower Temperature, higher measured mass
  1) Generally, lower T, higher density, higher mass (by 0.01 in our T range)
  2) Lower T, lower vapor pressure, less pressure build-up within pipette, less volumetric loss from pipette, higher mass
Conclusion: due to vapor pressure, some volume is lost in preparation, resulting in lower than expected mass measurements.
  Note: volumetric loss begins immediately after pipetting, even if the tip is still submerged
  Potential workaround : pre-wetting the tip.
Low T density check
Chart: T_bottle (C)
| 4.5 | 8 | 9.3000000000000007 | 10.3 | 10.5 | 21.1 | 21.1 | 21.1 | 21.1 | 21.1 | 21.1 | 21.1 | 21.1 | 21.1 | 21.1
Mass | 0.8227 | 0.8096 | 0.7949 | 0.8125 | 0.8001 | 0.7095 | 0.7184 | 0.7092 | 0.7156 | 0.7292 | 0.6925 | 0.7043 | 0.7082 | 0.7133 | 0.688
T bottle (C) | Mass (g) | Theoretical Density (g/cm3) | Difference
4.5 | 0.8227 | 0.9130 | -0.0903
8.0 | 0.8096 | 0.9112 | -0.1016
9.3 | 0.7949 | 0.9104 | -0.1155
10.3 | 0.8125 | 0.9099 | -0.0974
10.5 | 0.8001 | 0.9098 | -0.1097
21.1 | 0.7095 | 0.9034 | -0.1939

## Slide 5
2.9 wt% is wild
2.0 wt% is not as wild
  BUT 2.0 wt% melt peak at 273.4 K, wt% undetermined by liquidus
Minor tweaks to model
  Low wt% behavior changes by quite a bit
  Will check changes again
2.0 wt%, 2.9 wt%

## Slide 6
2.0 wt%, 4.03 wt%
Using lab derived wt%, later experiments (with new bottle) have better agreement

## Slide 7
Thought process:
  Measurement-derived wt% are unreliable for old bottle experiments (top 5/6)
    Due to unconstrained old supply bottle wt% and density
  Measurement-derived wt% may not be reliable for new bottle
    Unconstrained volumetric loss from pipette during preparation
  Liquidus-derived wt% are highly erroneous for low wt % (< 5 wt%, err >10 %)
    Due to 0.5 K uncertainty in T, error propagated onto wt % is large, which greatly determines Cp’s variation. OR
    Model breaks down at low wt% (uncertainty of model?)
  Keep liquidus-derived wt%, discard <5 wt% values.
2.0 wt%, 4.03 wt%

## Slide 8
Thought process:
  Measurement-derived wt% are unreliable for old bottle experiments (top 5/6)
    Due to unconstrained old supply bottle wt% and density
  Measurement-derived wt% may not be reliable for new bottle
    Unconstrained drips from pipette in preparation
  Liquidus-derived wt% are highly erroneous for low wt % (< 5 wt%, err >10 %)
    Due to 0.5 K uncertainty in T, error propagated onto wt % is large.
  Keep liquidus-derived wt%, discard <5 wt% values.
2.0 wt%, 4.03 wt%
wt % | error | % error
*1.42 |  | 
*2.0 |  | 
2.5 | 0.45 | 18.0
2.9 | 0.4 | 13.8
4.9 | 0.5 | 10.2
7.9 | 0.3 | 3.8
8.1 | 0.3 | 3.7
9.7 | 0.3 | 3.1
14.2 | 0.3 | 2.1
20.0 | 0.2 | 1.0
26.9 | 0.1 | 0.4

## Slide 9
Based on heatflow and T sensitivity of 0.1 µW and 0.1 mK, mass error of 0.1 mg
In melt, lower wt %, lower error
In liquid, larger T profile (46 C), larger T interval per step, lower error.
Cp Errors

## Slide 10
Based on heatflow and T sensitivity of 0.1 µW and 0.1 mK, mass error of 0.1 mg
In melt, lower wt %, lower error
In liquid, larger T profile (46 C), larger T interval per step, lower error.
Melt Cp errors incomplete: - errors from latent heat of fusion of ice not yet accounted for (SeaFreeze).
Cp Errors

## Slide 11
Based on 0.5 K reported by Victoria (0.1 K/min). How?
  Will be taking onset T for the pure ice run tomorrow from Calisto
  ADH onset T at 0.1 K/min errors are <0.05 K
  BUT 1.42 wt% and 2.0 wt% runs, the liquidus are >0.05 K greater than 273.15K
Wt % errors
wt % | error | % error
*1.42 |  | 
*2.0 |  | 
2.5 | 0.45 | 18.0
2.9 | 0.4 | 13.8
4.9 | 0.5 | 10.2
7.9 | 0.3 | 3.8
8.1 | 0.3 | 3.7
9.7 | 0.3 | 3.1
14.2 | 0.3 | 2.1
20.0 | 0.2 | 1.0
26.9 | 0.1 | 0.4

## Slide 12
As I write, questions pop up. For now, I’ll collate them as comments in the overleaf project, for discussion points during these meetings
For simpler questions, I’ll email relevant people as and when they appear.
Timeline:
  Nov 24:
    Complete Introduction, Experimental Methods, Results
    Review of Tillner-Roth and Friend comparison
    Meeting to lay out Discussion and application to planetary science
  Dec 8:
    Complete Discussion and Conclusion
    Meeting to review contents
Manuscript Draft

## Slide 13
What are the next steps for comparison with Tillner-Roth and Friend?
I will, keep liquidus-derived wt%, discard <5 wt% values. Is that okay?
Ticket Items

## Slide 14
Affects Cp results:
  Ice Cp being lower than literature
  Density measurements being lower than lit
Does not affect Cp results:
  ADH double peaks
Unanswered Questions