## Slide 1
Glovebox Experiments
Averaging
Deviations from literature
Calorimeter T Uncertainty
Decide wt% determination process
Anomalous Data
Summary

## Slide 2
Goal – Explain drip from pipette
Challenges:
  Recorded T varies wildly when N2 gas is being pumped into box
  Solution had to be drawn into pipette very slowly to prevent spurting
Key observation:
  No apparent volumetric loss at <0 C
Conclusion:
  Volumetric loss via drips accounts for most of density difference from theoretical
  Drips due to vapor pressure (at 20C, it’s ~3.1 times greater than at -10C)
  ~0.05 g difference from theoretical (0.91)
Glovebox Experiments
T_box | T_Bottle | T_Cell | Mass | Vol Loss?
-10 | -8.1 | -10 | 0.8626 | 0 drips
-10 | -3 | -4.1 | 0.8718 | 
-10 | -4.3 | -6.4 | 0.8455 | 
0 | -6.8 | -5.2 | 0.8492 | 
0 | -2 | 6 | 0.8216 | 
0 | -5.4 | -1.8 | 0.8628 | 
10 | 4.5 | 11 | 0.8304 | ~1 drip
10 | 4.7 | 12.3 | 0.8326 | 
10 | 7 | 13.6 | 0.8442 | 1 drip
20 | 18 | 13.4 | 0.7446 | ~3 drips
20 | 19.5 | 14.8 | 0.7666 | 
20 | 20.1 | 16 | 0.7563 | 3 drips
Chart: T (C)
| -10 | -10 | -10 | 0 | 0 | 0 | 10 | 10 | 10 | 20 | 20 | 20
 | 0.8626 | 0.8718 | 0.8455 | 0.8492 | 0.8216 | 0.8628 | 0.8304 | 0.8326 | 0.8442 | 0.7446 | 0.7666 | 0.7563

## Slide 3
Supply Bottle:
  We have been using A667-212  NF/FCC Grade
  Reported by Munoz-Iglesias 2018 is ACS Certified Plus Grade (A669-500)
Glovebox Experiments

## Slide 4
Reasons for variability:
  Melt: propagated variability in calculations: d_T, d_crystalFraction
Average smoothing (moving mean, 1 K mean)

## Slide 5
Reasons for variability:
  Melt: propagated variability in calculations: d_T, d_crystalFraction
  Both: variability in blank – blank subtraction not perfect, noise variable for different runs (can I use deviations between blank HF as calorimeter noise?)
Average smoothing

## Slide 6
Reasons for variability:
  Melt: propagated variability in calculations: d_T, d_crystalFraction
  Both: variability in blank – blank subtraction not perfect, noise variable for different runs (can I use deviations between blank HF as calorimeter noise?)
Average smoothing

## Slide 7
Kink at ~295 K:
  explained by Tuan in Vu 2019 “This very slight difference between the two thermopiles tends to introduce additional noise that is most prominent around room temperature”
Average smoothing

## Slide 8
Which should we proceed with/report?
  I would say discrete 1 K average points are most digestible.
Average smoothing

## Slide 9
Tighter spread
Deviations from TRF (mass fraction)

## Slide 10
Tighter spread
Deviations from TRF (mass fraction)

## Slide 11
Tighter spread
Deviations from TRF (Temperature)

## Slide 12
Tighter spread
Deviations from TRF (Temperature)

## Slide 13
Goal – Confirm 0.5 K uncertainty reported by Victoria
Other peaks at low T approx. similar deviation
H2O peak deviation is large and always positive
Can we subtract 0.5 K offset for measured peaks, and retrieve accurate wt%?
  -0.5 K until what lower T bound? (e.g. 20 wt%, peak at 235 K)
  For the 0.5 K number itself, what is it’s uncertainty?
Calorimeter T Uncertainty
Chart: Theoretical T (K)
| 164.75
THF | 0.048
ADH | -0.016 | -0.012 | -0.15 | -0.001 | -0.02 | -0.045 | 0.054 | 0.013 | 0.024 | -0.017 | -0.001 | 0.18 | 0.007
CP | 0.013 | -0.086
H2O | 0.667 | 0.566

## Slide 14
Low wt% (<2.0 wt%) still has measured peak > 273.15 K, doesn’t make sense.
0.5 K of H2O measured by onset peak, but our experiments use min peak, additional unconstrained offset.
Lower wt%, larger H2O wt%, greater peak, greater onset – min difference.
Calorimeter T Uncertainty
No offset
-0.5 K offset

## Slide 15
Decision on how to determine wt%
Can we conclude T offset is always positive at liquidus temperatures?
Can we assume T offset is consistent from 230 K to 273 K?
Can we take +0.5 K as T offset, with no error?
Do ~2 pure H2O runs to characterize T error
Use 0.5 K as T error, throw away data <5 wt% (n=6), due to 1. sensitivity of wt% to T, and 2. large onset – min peak difference
Get wt% based on T – offset, and throw away <3.0 wt% (n=4) due to large onset – min peak difference
Find other solutions with peaks at ~230-250 K to determine T offset dependence on peak T
Get wt% based on T – offset, reporting T error and throw away <3.0 wt% (n=4) due to large onset – min peak difference
Get wt% based on variable T – offset, and throw away <3.0 wt% (n=4) due to large onset – min peak difference
Get wt% based on T – offset for <5 wt%, and throw away <3.0 wt% (n=4) due to large onset – min peak difference
Can we constrain onset – min peak difference?
no
yes

## Slide 16
Mostly at low wt%
L shape: increase lower T bound
Red (2 wt%) greater than others
Purple (2.9 wt%) decreasing
Green (4.9) and Light Pink (4.91) are different
Discuss reasons for these anomalies?
Anomalies
Errors of ~0.34% accounts for ~0.01 difference, so it cannot explain the differences (or error propagation is incorrect). For example, variability of heatflow between runs not accounted for (from discussion above about blanks)

## Slide 17
Glovebox Experiments
  Volumetric loss via drips accounts for most of density difference from theoretical
Averaging
  Calorimeter noise unconstrained. Use blank heatflow variability to represent
  Report discrete 1 K average points.
Deviations from literature
  Awaiting further discussion
Calorimeter T Uncertainty
  Reported 0.5 K is always positive
Decide wt% determination process
  Final decision should be reached.
Anomalous Data
  Discussion depends on wt% determination and calorimeter noise.
Summary