## Slide 1
Double Peak
Peak Temperatures
Cp linear combination
Summary

## Slide 2
DP appears in 3.52wt%, 8wt%
Small wiggle after main peak in most samples
Double Peaks

## Slide 3
Small peak wiggles after the main peak is seen across most samples, including 0wt%
Double Peaks
0wt%
1.76wt%
3.52wt%
6wt%
8wt%
10wt%

## Slide 4
Rerun of 3.52wt% produced no double peak
Potential reasons:
  Sample was not well mixed, causing inhomogeneous crystallization
  Contamination (unlikely)
Double Peaks

## Slide 5
Small wiggles can be disregarded (?)
Double peak likely an experimental anomaly
  Suggestion: re-run 8wt% and confirm (non-)existence of DP for that sample
Double Peaks Conclusions

## Slide 6
Peak Temps
 | Onset Temps |  |  | 
Samples | AMH Melt | Offset | ADH Melt | Offset
1.76 wt.% | 171.18 | 0.18 | 177.19 | 1.06
3.52 wt.% | 171.07 | 0.07 | 176.53 | 0.40
3.52 wt.%_2 | 172.74 | 1.74 | 178.67 | 2.54
6 wt.% | 170.62 | -0.38 | 176.49 | 0.36
8 wt.% | 170.71 | -0.29 | 176.52 | 0.39
10 wt.% | 170.15 | -0.85 | 176.71 | 0.58
Theoretical | 171 |  | 176.13 | 
 | AMH |  | ADH | 
Samples | H2O liquidus | Peak 1 | Offset | Peak 2 | Offset 2
1.76 wt.% | 271.76 | 278.29 | 6.53 |  | 
3.52 wt.% | 269.64 | 272.19 | 2.55 | 277.48 | 7.84
3.52 wt.%_2 | 269.64 | 274.56 | 4.92 |  | 
6 wt.% | 266.02 | 269.50 | 3.48 |  | 
8 wt.% | 262.64 | 260.09 | -2.55 | 267.31 | 4.67
10 wt.% | 259.07 | 259.66 | 0.59 |  | 
0 wt.% | 273.15 | 282.20 | 9.05 |  | 
Peak Temps for AMH/ADH phase change somewhat within uncertainties (<1K)
Peak Temps for water ice phase change very variable
How do we use this information to determine how much to offset?

## Slide 7
A brief overview of the lever rule The crystal fraction () is obtained via:
For e.g with 10wt% sample,
At peritectic (176K),
At 200K,
At liquidus (259K),
Liquidus curve equation from Croft et al. 1987
Fraction of Crystals
The Fc curves obtained

## Slide 8
Total energy absorbed (integral of heat flow) a linear combination of:
Latent heat (ice) * mass of the crystal fraction that have melted in time step
Specific heat of crystal (ice) * mass of crystal fraction present * change in temperature over time step
Specific heat of liquid * mass of liquid fraction present * change in temperature over time step
Linear Combination

## Slide 9
Calculated within T-range with valid Fc (theoretical partial melting range)
(note its at 273.15K/1atm)
based on data by Feistel & Wagner 2006 (10K interval)
Linear Combination

## Slide 10
Fc range intersects ADH melting (176K)
Liquidus point (~269.64K) before peak heatflow (~274.56K)
Linear Combination

## Slide 11
Arbitrary offset: aligning peak heatflow to liquidus point
Linear Combination

## Slide 12
Arbitrary offset: aligning peak heatflow to liquidus point
  For other samples, graphs found in Github repo ~/o_specificHeat/
Linear Combination

## Slide 13
wt% (X) is proportional to T
  Regardless of wt% used in runs, the wt% of liquid phase at a particular T in the partial melting regime is fixed (it runs along the liquidus)
Linear Combination

## Slide 14
wt% (X) is proportional to T
  Regardless of wt% used in runs, the wt% of liquid phase at a set T in the partial melting regime is fixed.
Linear Combination

## Slide 15
Determining correct method for temperature offset
Determining if cp equations makes sense
Clarifying objective of current experiment
  Determining cp of H2O-NH3 at 176-273K, 1atm.
From cp  Gibb’s Free Energy  Minimization of GFE  EOS
Long Term Plan of the primary project I’ll be working on
  Provide as much data possible for PlanetProfile (Ocean thermodynamic data for NH3, possibly other organics/salts)
  Specific Heat  EOS  other thermodynamic properties required for PP
  Plan to have a meeting with Steve & Mathieu when Steve’s back
Next Steps

## Slide 16
0wt%, 2.5ml, 0.1K/min
Blank, 0.1K/min
8wt%, 2.5(?)ml, 0.1K/min
Other wt%
Next Steps