## Slide 1
Plot of measured heat flow over temperature
Endothermic and exothermic peaks indicate phase transitions
Chose to characterize specific heat in ice Ih partial melting regime (~185K to ~280K)
Summary
1
2
3
4
5
Glass transition,
2) NH3H2O melting,
3) NH32H2O forming
4) NH32H2O melting,
5) H2O partial melting

## Slide 2
Plot of calculated specific heat capacity of liquid over temperature
General expected increasing trend, with extremes near phase transition peaks
Summary

## Slide 3
Total energy absorbed (integral of heat flow) a linear combination of:
Energy to melt ice
Energy to heat ice
Energy to heat solution
  We’re finding this specific heat
Linear Combination

## Slide 4
Calorimeter:
Re-running experiments at lower temperature ramp rate
Determine temperature shift corrections (due to lag time of melting)
Others:
Meeting with Richard Otis to (start to) understand PyCalphad
Learning Perple_X
Current work