## Slide 1
Experiment Plans
Results
Discussion
Main Updates

## Slide 2
Motivation: current dataset has a kink (calorimeter systematic error), which breaks up trend. Goal is to obtain data beyond 310 K to extend trend.
Experiments Plan

## Slide 3
One experiment a week.
6 Experiments by end-Feb
Prioritize on:
  Extending 291 K data (8.4, 10.0, 26.912 wt%)
  Checking off-trend data (5.2 wt%)
2 additional experiments
  Vary wt%, or repeat previous experiments
Experiments Plan

## Slide 4
Goal for this discussion:
  Refine current write-up points for results
  Identify other points we may expand on
Liquid domain Cp
  Comparison with Tillner-Roth & Friend
Partial melting domain Cp
Thermogram observations
  Liquidus double peak
  ADH double peak
Results

## Slide 5
Liquid domain Cp:
Generally increasing with increasing T
Higher wt%, steeper gradient
Change in gradient for 14.3, 20.07 wt% at 285 K
Above 285 K, Cp is proportional to wt% (except 5.2 wt%)
Below 285 K, higher wt% Cp values cross below lower wt%
Above 273.15 K, all Cp above that of water
Results

## Slide 6
Comparison with Tillner-Roth & Friend:
Deviation consistently with 10% on both T and wt% axes.
Trend in deviations along T axis.
  “increasing trend”
Cp from EoS for low wt%, at <300 K, increase with decreasing T.
  May be due to EoS construction using supercooled H2O?
EoS not reliable in prediction low T, low wt% Cp.
Results

## Slide 7
Comparison with other data (?):
33, 49 – 65 wt%.
  All datapoints higher than 33 wt%.
1 – 33 wt%, 275 – 334 K.
  Cp ranges from 4.04 – 4.29 J/gK
  Generally, our data is higher (4.26 – 4.5)
Results

## Slide 8
Partial Melting Domain Cp:
General agreement with higher wt% datasets
Low wt% datasets have greater Cp, that diverges at higher T
All datasets almost fall within 1-sigma error of each other
Overall fit falls within errors
Small uptrend of Cp due to combination of higher Cp with higher T and lower Cp with lower wt%.
Results

## Slide 9
Thermogram observations (?):
Liquidus double peak:
  Due to poor mixing, inhomogeneous crystallization
  Crystal melt at different times and rates, hence double peak
ADH melting double peak:
  Low wt%, more pronounced
  Low wt%, inhomogenous crystallization of ADH
  At higher ramp (0.25 K/min), not observed due to low T-resolution
Results

## Slide 10
Interior Models:
Extrapolate our low T, low wt%, 0.1 MPa data to higher pressures:
  Current EoS underestimation of Cp > 280 K, overestimation of Cp <280 K.
  Shallow region of ocean with NH3  cooler (Tb ~250 K), lower Cp than modelled.
  Deeper regions  warmer, higher Cp than modelled.
  Overall higher Cp of ocean  more heat required to warm ocean  colder temperature profile  thinner ocean.
Thermal evolution models  higher Cp, longer time required for cooling and crystallization
Usefulness of partial melting domain data:
  Melt pockets in ice-shells?
Discussion

## Slide 11
Ice Shells
Considering the T-range of our study, applicable to base of ice shells (partial melting domain)
Cometary Studies
Discussion here primarily due to our data being low pressure.
Discussions on volatilization of NH3
Discussion (Low Pressure)